## Slide 1: Particle pollution in Italian ports & experiences from Northern European ECA
Kare Press-Kristensen
M.Sc. in engineering, Ph.D.
Senior advisor on air quality
Green Transition Denmark
kaare@rgo.dk

## Slide 2: Health effects of air pollution in Italy
Around 65,000 people die from air pollution every year in Italy (EEA, 2020). That is 10.5% of all deaths (630,000).
In 2020-22 air pollution (195,000) killed more people in Italy than COVID (180,000). No vaccine against pollution.
If air pollution from shipping causes just 10% of deaths due to air pollution shipping kills 6,500 Italians per year.
Cancer, cardiovascular diseases and airway diseases etc.
It is very cost effective to reduce air pollution from ships.

## Slide 3: Shipping is poorly regulated
Chart: Sulphur in marine fuels vs. road fuel
| Former global limit | Former global average | SECA limit 2010-14 | Global limit 2020 | SECA limit 2015 | Road transport 2010 (EU)
 | 35000 | 25000 | 10000 | 5000 | 1000 | 10
2014: All new trucks in EU have very effective exhaust gas cleaning systems – no ships have filters or catalytic converters !

## Slide 4: Trucks have filters – Ships have no filters
Piombino
Oct. 6th, 2021
Wind: 6-8 m/s.
Ships have no filters. A cruise ship (4,000 p.) at berth emits as many particles as 5,500 cars per second.

## Slide 5: Soot from shipping (pictures from Genoa 2016)

## Slide 6: Genoa: A cocktail of bad conditions
A lot of polluting ferries and cruise ships inside the heart of the city for most of the year.
The city almost covers a circle around the port so pollution plumes will hit residential areas most of the time.
City is built uphill, so chimneys are in same height as windows.
Have a warm climate so people spend much time outdoor, and windows are open when it is warm = when you have cruise ships.
Still no shore power for cruise ships and ferries.

## Slide 7: Measurements: Ultrafine exhaust particles

## Slide 8: Measurements of air quality in Italy
Measured ultrafine exhaust particles.
Particles smaller than 100 nm consisting of soot (black carbon) coated with PAHs and heavy metals.
Ultrafine particles are deposited in the finest parts of the lungs (alveoli) and transferred into the blood.
Clean air in Europe contains 1,000-3,000 particles per cm3.

## Slide 9: Genoa with/without cruise ship: 6-10 m/s
With cruise ship
Without cruise ship

## Slide 10: Genoa upwind cruise ship ferry: 9 m/s
Genoa, October 24, 2022

## Slide 11: Livorno upwind and downwind ferry: 11 m/s
Down-wind: After ship
Up-wind: Before ship

## Slide 12: Piombino upwind/downwind ferry: 6-8 m/s
Down-wind: After ship
Up-wind: Before ship

## Slide 13: 2021: Civitavecchia with/without wind from sea
8 m/s from West: Oct. 6th
No wind: Evening Oct. 1st

## Slide 14: 2021: Civitavecchia with/without wind from sea
8 m/s from West: Oct. 6th
No wind: Evening Oct. 1st

## Slide 15: Civitavecchia: The pollution hits the city
8 m/s from West: Oct. 6th 2021

## Slide 16: Results from measurements
Shipping cause significant pollution of Italian port cities.

## Slide 17: Measurements from Civitavecchia

## Slide 18: Measuring report
Report with screening measurements from Italian port cities:
https://rgo.dk/wp-content/uploads/Air-pollution-from-shipping-in-Italian-ports.pdf

## Slide 19: Emission control area in Northern Europe
SOx Emission Control Area from 2007 with the strictest sulphur limit from 2015.
NOx Emission Control Area from 2021 for all new build ships.

## Slide 20: Measurements from Northern Europe
Measurements from Neuwerk (German island)
Before SECA
After SECA
Concentrations of toxic SO2 immediately dropped, as expected, after introducing the SECA

## Slide 21: Control and enforcement
EU: - Min. 10% inspections and 4% sulphur analysis.
- Fines must prevent systematic violations.
DK: - Helicopters measuring sulphur, NOx and CO2 directly in the ship exhaust fan at sea (600/yr.).
- Name and shame on ship/companies violating.

## Slide 22: Conclusions from Northern European ECA
Plenty of distillate fuel (0.1% sulphur) available.
High reduction in sulphur on land (50% drop in 2015).
Significant health and economic benefits for society.
No enforcement challenges (0.0067% violations).
No cargo transfer from ship to road.
No notable price increases for consumers (< 0.005%).
No notable extra costs for ship owners or authorities.

## Slide 23: Solutions for ship pollution
In ports:
Shore power for cruise ships, ferries, cargo ships, etc.
At sea:
Electric ferries – Great potential.
Particulate filters for ships (removes > 95%).
Emission Control Areas (ECAs) limiting emissions:
- SO2 emissions will drop 80% immediately.
- NOx emissions will drop 80% over 20-25 years.
- Particle emissions will drop significantly and immediately.

## Slide 24: Shore power in Northern Europe

## Slide 25: Electric ferries in Denmark

## Slide 26: With support from EU: LIFE4MEDECA
This presentation is part of the EU LIFE project: LIFE4MEDECA with the purpose to designate a Mediterranean Sea Emission Control Area to reduce health hazardous and climate damaging emissions of air pollution from ships.

## Slide 29: NOx from ships in Northern Europe
Adverse health effects: 42 € per kg NOx emission.
Removal costs: 2 € per kg NOx removed (using SCR).
Society saves around 42 billion € in health damages every time society invests 2 billion € in NOx-removal
 Rate of return: 2.000% !
+ less damages on crops, constructions, ecosystems, etc.
A NOx ECA is the best investment you can imagine …

## Slide 30: Control and enforcement
EU: - Min. 10% inspections and 4% sulphur analysis.
- Fines must prevent systematic violations.
DK: - Helicopters measuring sulphur, NOx and CO2 directly in the ship exhaust fan at sea (600/yr.).
- Name and shame on ship/companies violating.

## Slide 31: Shore power in Northern Europe

## Slide 32: Electric ferries in Denmark

## Slide 33: Shipping is poorly regulated
Chart: Sulphur in marine fuels vs. road fuel
| Former global limit | Former global average | SECA limit 2010-14 | Global limit 2020 | SECA limit 2015 | Road transport 2010 (EU)
 | 35000 | 25000 | 10000 | 5000 | 1000 | 10
2014: All new trucks in EU have SCR & particulate filters!